## Slide 1
Fluorescent wavefront shaping using incoherent iterative phase conjugation
Anat Levin
Department of Electrical Engineering
Technion
Joint work with Dror Aizik and Ioannis Gkioulekas
Notes: My name is Anat Levin and I will tell you today about a novel and fast approach for wavefront shaping.

## Slide 2
Camera
Scattering: the largest barrier to tissue imaging
Tissue
Camera image
Cannot see inside
incident laser illumination
Notes: Imaging inside our body is very hard because incident illumination is scrambled by the internal components of the tissue. As a result, a camera will only see a noisy scattered pattern rather than the actual structure.
A lot of research efforts were devoted to the problem, and today we are going to talk about a particularly attractive approach, known as wavefront shaping.
And let me start by explaining what is wavefront shaping.

## Slide 3
Fluorescent Beads
Main system Camera
Image through thin tissue
Tissue
Wavefront shaping principles
Emission wave
Excitation wave
Focus through thin slice
Excitation laser source
Notes: We want to see fluorescent cell components inside tissue.
When we illuminate tissue, such fluorescent components are excited and emit light at a different wavelength. This new color allows biologists to distinguish them from the rest of the tissue.
In this talk we are going to address single photon fluorescence, meaning that the amount of energy emitted from a fluorescent point is scaled linearly with the excitation energy arriving it.
If the tissue is thin, the camera can see the fluorescent sources crisply.
We can also control the illumination and bring all of it into a single spot for laser treatment therapy.

## Slide 4
Image through thin tissue
Main system Camera
Emission wave
Excitation wave
Image through thick scattering tissue.
Excitation laser source
Wavefront shaping principles
Fluorescent Beads
Tissue
Cannot focus
Notes: However, if the tissue layer is thick, we cannot focus the excitation beam in a single spot, as it scatters before it gets there.
Also the light emitted from the sources, scrambles quite a lot in the tissue and the camera sees just a noisy speckle pattern.

## Slide 5
Image through thin tissue
Main system Camera
Emission wave
Excitation wave
Image through thick scattering tissue.
Modulation element
Image thr. thick tissue + correction element
Undo scattering
Same pattern
Excitation laser source
Wavefront shaping principles
Fluorescent Beads
Tissue
Notes: The idea of wavefront shaping is that we can place a computer controlled modulation element between the tissue and the camera, that will correct the tissue aberration and will allow us to see a sharp image of the sources.

## Slide 6
Image through thin tissue
Main system Camera
Emission wave
Excitation wave
Image through thick scattering tissue.
Modulation element
(SLM)
Image thr. thick tissue + correction element
Same pattern
Focus through thick slice
No practical algorithm for finding correction element.
Very costly optimization.
Excitation laser source
Wavefront shaping principles
Undo scattering
A. Boniface et al “Noninvasive light focusing in scattering media using speckle variance optimization,” Optica. (2019)
T. Yeminy and O. Katz, “Guidestar-free image-guided wavefront-shaping,” Sci. Adv. (2021).
G. Stern and O. Katz, “Noninvasive focusing through scattering layers using speckle correlations,” Opt. Lett. (2019).
A. Daniel et al. “Light focusing through scattering media via linear fluorescence variance maximization, and its application for fluorescence imaging,”Opt. Express (2019).
Fluorescent Beads
Tissue
Notes: In the same way we can place a modulation element in the illumination path that will aberrate the illumination wavefront in a way which is exactly the inverse of the aberration process in the tissue, so that when this aberrated wavefront propagates through the tissue it will actually focus into one spot.
Wavefront shaping is a very exciting idea because if this can be done any scattering process can be inverted.
But in practice there are no good algorithms for finding the desired modulation.
Existing approaches rely on iterative algorithms which need to image thousands of trial modulation patterns before they converge.

## Slide 7
Image through thin tissue
Main system Camera
Emission wave
Excitation wave
Image through thick scattering tissue.
Image thr. thick tissue + correction element
Same pattern
Our approach: fast, non invasive computation of correction element.
From laser
This work: fast wavefront shaping
Modulation element
(SLM)
Undo scattering
No practical algorithm for finding correction element.
Very costly optimization.
Fluorescent Beads
Focus through thick slice
Notes: In this research, for the first time, we suggest a fast algorithm that can recover the modulation element with a very small number of iterations.

## Slide 8
Main system Camera
Emission wave
Excitation wave
From laser
Results
Validation Camera
initialization
Itr 1
Itr 2
Itr 3
Itr 4
Excitation
Validation camera
Fluorescent Beads
Tissue
Notes: Before I talk on how to do that, let me start by showing some results.
In order to better show you what is happening here I put the fluorescent beads at the back of the tissue layer and not really inside it, and I put another validation camera behind the tissue, which can image the beads directly. The validation camera does not provide any feedback to the algorithm and is only used to assess its success.
So we start with some random modulation pattern and when this pattern scatters through the tissue we get a wide speckle pattern at the back layer. But based on the image we capture at the main camera we update our modulation and with as little as 4 iterations, the modulated illumination focuses into a single spot behind the tissue.

## Slide 9
Emission wave
Excitation wave
From laser
Results
Validation Camera
Main system Camera
Filter emission wavelength
initialization
Itr 4
Excitation
. . .
Validation camera
Tissue
Notes: Now to save space I will squeeze this sequence and show only the first and last iterations.
To show you the fluorescent beads themselves I put a bendpass filter so we only see the emission light and not the excitation.

## Slide 10
Emission wave
Excitation wave
From laser
Results
Validation Camera
Main system Camera
Filter emission wavelength
Validation camera
initialization
Itr 4
Excitation
. . .
Emission
. . .
Tissue
Notes: So you can see that there is a spread of beads here, in the beginning many of them are excited, but as we proceed the excitation light is focused into one spot and as a result only one of the beads emits light.
Now the decision on how to update the modulation is not based on what the validation camera is seeing but on what the main camera from the other side sees, and let’s have a look at what this camera can image

## Slide 11
Emission wave
Excitation wave
From laser
Results
Validation Camera
Main system Camera
Validation camera
Main camera
initialization
Itr 4
Excitation
. . .
Emission
. . .
No mod.
. . .
Tissue
Notes: We note that even if we manage to focus all the light and excite a single bead, the light will scatter on its way back to the camera, and in the main camera we see yet another speckle pattern.

## Slide 12
Emission wave
Excitation wave
From laser
Results
Validation Camera
Main system Camera
Validation camera
Main camera
initialization
Itr 4
Excitation
. . .
Emission
. . .
No mod.
. . .
Tissue
Notes: However if we take the modulation used in the illumination arm and also place the same pattern in the imaging arm we can correct the aberration.

## Slide 13
From laser
Emission wave
Excitation wave
Results
Validation Camera
Main system Camera
Validation camera
initialization
Itr 4
Excitation
. . .
Emission
. . .
No mod.
. . .
Main camera
Tissue
Notes: we can correct the aberration.
So let’s see what this gives us.

## Slide 14
From laser
Emission wave
Excitation wave
Results
Validation Camera
Main system Camera
Rapid convergence
Validation camera
Main camera
initialization
Itr 4
Excitation
. . .
Emission
. . .
No mod.
. . .
With mod.
. . .
Tissue
Notes: As the iteration proceed and the excitation focus into a single bead, the emission is also corrected and we see a sharp spot on the main camera.
So this algorithm converges into a focusing modulation within a very small number of iterations, and this is a big improvement over previous approaches.

## Slide 15
Main system Camera
Results: imaging a wider area
Emission wave
Excitation wave
same modulation for imaging
From laser
Temporal correlations
Optical coherent tomography
Seeing inside tissue
Material acquisition
Excite a wide area
Undo scattering of emitted light
Validation Camera
speckle correlations=> same modulation can correct neighboring sources
Tissue
Notes: Now once we found the modulation for one spot, we want to use it to image a bigger area of beads behind the tissue and not just this one spot.
For that we use the modulation only in the imaging arm. This means that the illumination is not corrected and it excites a wide group of beads. However the light which is scattered from each bead is corrected on its way to the camera.
Now the memory effect property of speckles implies that the same modulation can help us to correct a local area of fluorescent sources behind the tissue and not only the single bead from which it was computed.

## Slide 16
Main system Camera
Results: imaging a wider area
Emission wave
Excitation wave
same modulation for imaging
From laser
Temporal correlations
Optical coherent tomography
Seeing inside tissue
Material acquisition
Excite a wide area
Undo scattering of emitted light
Main camera with our modulation
Conventional image
Reference (validation camera)
Validation Camera
Tissue
Notes: So let’s see what we can get with that.
Here are two input speckle images
And here are the beads we managed to image with the main camera using the modulation we have recovered,
and for a reference, here is a direct image of the beads from the validation camera.
Let me mark some regions so you can better compare the result to the ground truth.
Note that the area we can image with one modulation has a limited extent. The further beads are not imaged, and you can also see that in the periphery of this region we start to get aberrations.
So after we have seen some nice things we can do, I want to move and talk about how we do it.

## Slide 17
Fluorescent Beads
Main system Camera
Output wavefront
Input wavefront
modulation element
From laser
Coherent iterative phase conjugation
Validation Camera
Reflective particles
C. Prada et al. “The iterative time reversal process: Analysis of the convergence,” The J. Acoust. Soc. Am. (1995).
H. C. Song, et al. “Iterative time reversal in the ocean,” The J. Acoust. Soc. Am. (1999).
K. Si et al. “Breaking the spatial resolution barrier via iterative sound-light interaction in deep tissue microscopy,” Sci. reports (2012).
H. Ruan et al. “Iterative time reversed ultrasonically encoded light focusing in backscattering mode,” Sci. reports (2014).
Tissue
Notes: So we use an algorithm called iterative phase conjugation. This algorithm was classically derived for coherent illumination. But fluorescent sources emit incoherent illumination. I will start by explaining the coherent case and then I will discuss the challenges and the benefits in adapting it to the incoherent case.
So let’s assume that instead of fluorescent beads we have behind the tissue some gold particles which reflect a lot of light.

## Slide 18
Reflective particles
Main system Camera
Output wavefront
Input wavefront
From laser
Coherent iterative phase conjugation
Validation Camera
output wave
input wave
back-plane wave
Transmission matrices
Even with focus: output=speckle
 How can we know we have focused?
Phase conjugation principle
back-plane
Tissue
output wave
input wave
output wave
Back-plane wave
Back-plane wave
input wave
Notes: With our computer controlled light modulator we can send in various illumination wavefronts. And each such wavefront generates some other wavefront at the back of the tissue.
To model the problem mathematically we consider the transmission matrix of the medium, which describes how each incoming wavefront is mapped into the back plane of the tissue.
Once the wavefront gets to the reflective particles at the back of the tissue it is reflected and scatters back through the tissue, and it generates an outgoing wavefront at the main camera.
We consider another transmission matrix To that maps between wavefront at the back plane, to wavefonts at the main camera.
For ease of visualization I use a different color for each of the 3 wavefronts but in practice the coherent case they are all at the same wavelength.
Overall we will be describing the mapping between incoming illumination to outgoing wavefront at the camera, by a transmission matrix T, which is the multiplication of Ti and To.
This model involves some approximation, and we will come back to what we have neglected here in a few slides.
So assuming this Ti To model, we use the principle of optical wave conjugation. It tell us that the wavefront coming out of a point, is the conjugate of the wavefront focusing at it, or namely that To is the transpose of Ti.

## Slide 19
Main system Camera
Output wavefront
Input wavefront
Focus
Excitation wave
Focusing wavefront is an eigenvector of transmission matrix
For a focusing illumination,
input wavefront
output wavefront
Phase conjugation principle:
=
Emission wave
From laser
Problem: we don’t know .
Measure eigenvectors directly!
Same pattern
Coherent iterative phase conjugation
Tissue
Reflective particles
Notes: We can show that this also means that if we managed to focus than the outgoing wavefront is equal up to a scale factor to the incoming wavefront.
In a mathematical terminology this means that the focusing wavefront is an eigenvector of the transmission matrix T
This is a nice result, but every tissue layer has a different transmission matrix and this transmission matrix is very complex and we don’t know it.
But, I will show that we can directly measure the eigenvectors without knowing T.

## Slide 20
Output wavefront
Input wavefront
Use power algorithm to compute eigenvectors.
Initial random excitation wave
Main system Camera
From laser
Coherent iterative phase conjugation
Focusing wavefront is an eigenvector of transmission matrix
Phase conjugation principle:
Computation performed in optics
Tissue
Reflective particles
Notes: For that we exploit the power algorithm, which is widely used to compute eigenvectors numerically. It starts with a random vector and apply T iteratively on it. One can show that this sequence converges exponentially fast to the largest eigenvector of T.
We do the same here, and moreover, we leverage the optics to do the computation for us.
We start by illuminating the tissue with a random wavefront u_0 and measure the output. And by that, the optics has computed for us T of u_0. This output will be our input in the next iteration.

## Slide 21
Output wavefront
Input wavefront
Next excitation wave
Main system Camera
From laser
Coherent iterative phase conjugation
Use power algorithm to compute eigenvectors.
Focusing wavefront is an eigenvector of transmission matrix
Phase conjugation principle:
Computation performed in optics
Tissue
Reflective particles
Notes: We take the next output and reuse it again. And so on.

## Slide 22
Main system Camera
Output wavefront
Input wavefront
Focus
Next excitation wave
Eigenvector=
focusing wavefront
From laser
Coherent iterative phase conjugation
Use power algorithm to compute eigenvectors.
Focusing wavefront is an eigenvector of transmission matrix
Phase conjugation principle:
Computation performed in optics
Rapid convergence
Tissue
Reflective particles
Notes: This algorithm converges to the largest eigenvector of the tissue transmission matrix.
And by that we managed to focus all the light in one spot.
This algorithm is known as iterative phase conjugation. And its main advantage is that it converges very fast.

## Slide 23
Tissue
Main system Camera
Output wavefront
Input wavefront
From laser
Problems with coherent approach
Validation Camera
output wave
input wave
Back-plane wave
Transmission matrices
Model assumes:
No multiple scattering between reflective particles
No backscattering from tissue structures
In this work:
Use fluorescent particles rather than reflective ones
Emitted light does not excite tissue again
As we filter only the emission wavelength, even in thick tissue backscattering from the tissue itself is not measured
Applies for thick layers
Applies only to thin layers
output wave
input wave
output wave
Back-plane wave
Back-plane wave
input wave
Notes: So far I have discussed iterative phase conjugation assuming a fully coherent illumination.
But the coherent case has a problem that I have ignored earlier, and I now want to explain it.
To model the transmission of light in the tissue we considered a transmission matrix Ti, from the input wavefront to the particles behind the tissue, and another transmission matrix To, from the particles back to the sensor. And we assumed that the total propagation of light in the tissue can be described as the product of Ti and To. This model effectively assumes that there is no multiple scattering between the particles. And moreover, that there is not a lot of backscattering from other components of the tissue. This has limited previous experimental applications of this idea to thin and sparse scenes, where light scatters only once.
To overcome this problem, in this work we aim to focus at fluorescent sources and not at arbitrary reflective particles.
This relax the problem, because the emitted light does not excite the neighboring fluorescent sources again. Also, since the light emitted from the fluorescent sources have a different wavelength, we can filter only this wavelength and we do not measure all the scattering from the tissue itself.
Therefore, with fluorescence, the model can apply for thick tissue layers.

## Slide 24
Challenges in the incoherent case
Coherent
Linear light transmission
Camera measures
Incoherent
Non-linear light transmission
Excitation light at fluorescent spots
Camera measures emission
Our contribution: incoherent iterative phase conjugation, despite non-linearity
Notes: But using fluorescent sources pose a different problem. In the coherent case we can describe the propagation of light using a linear transmission matrix. But in the fluorescent case the wavefronts sums incoherently and that breaks the linear model.
Power iterations are designed for linear operators and if light propagation is no longer linear, it is not clear how they can be applied.
Our contribution is in showing that despite the non-linearity, we can apply iterative phase conjugation using incoherent sources.
Moreover, we show that perhaps surprisingly, this non-linearity actually accelerates the convergence.

## Slide 25
Convergence rate
Theorem
Coherent iterative phase conjugation converges as an exponential series
Incoherent iterative phase conjugation converges as a doubly exponential series
where denotes power at the kth particle at the tth iteration.
Notes: We prove the following theorem showing that in the coherent case the process converges as an exponential series. But in the incoherent case it converges asymptotically faster, as a doubly exponential series.

## Slide 26
Convergence rate
Typically, 2-6 iterations
Total convergence: 10-30 images
Previous wavefront shaping approaches: thousands of images
initialization
Itr 1
Itr 2
Itr 3
Itr 4
Excitation
Validation camera
Emission
Each iteration uses 5 images to estimate phase
Notes: In our implementation this converged within about 2-6 iterations.
Now there is another issue, which is that to update the modulation we need the phase of the wavefront and not only intensity. To address this, we capture 5 different variants of the same excitation pattern and use a phase diversity optimization to compute phase.
This phase acquisition approach is not optimal, and it is well possible that it can be accelerated.
As each update iteration requires 5 images, overall, we need to capture about 10-30 images in order to recover the wavefront shaping modulation pattern.
This is orders of magnitudes faster than previous wavefront shaping approaches which captured thousand of trial images before they managed to focus.

## Slide 27
Challenges in our approach
Currently applies only for a sparse set of incoherent sources.
initialization
Itr 1
Itr 2
Itr 3
Itr 4
Excitation
Validation camera
Emission
Notes: I would like to acknowledge one limitation of our approach. Which is, that currently, the set of fluorescent sources it can handle should be rather sparse, and we explain the problem in detail the paper.

## Slide 28
Summary
Fast estimation of wavefront shaping modulation
Modulation: eigenvector of transmission matrix, use power iterations
Incoherent emission accelerates convergence
Orders of magnitude speed up compared to previous strategies
Can use one modulation to image a region behind the tissue
Image with our modulation
Conventional image
Reference (validation camera)
Notes: So we got to the end of this talk and let me summarize the main contributions.
In this work we have proposed an extremely fast approach for computing a wavefront shaping modulation. It relies on the observation that the desired modulation is an eigenvector of the transmission matrix of the tissue, and it uses power iterations to compute it quickly.
While power iterations usually apply to linear operators, we adapt them to the incoherent case which is not linear. And we show that perhaps surprisingly, this non-linearity actually accelerates convergence.
Overall, this algorithm is orders of magnitude faster than previous approaches.
Another thing I have shown earlier is that due to the memory effect, once we found a wavefront shaping modulation, we can use it to image a modest region of beads behind the tissue, and not only a single spot.

## Slide 29
Paper
Fluorescent wavefront shaping using incoherent iterative phase conjugation
Dror Aizik, Ioannis Gkioulekas, Anat Levin
Image with our modulation
Conventional image
Reference (validation camera)
Scan me
Notes: Thanks for your attention, and you can scan this QR code to get to the paper.

## Slide 30
Image through thin tissue
Fluorescent Beads
Main system Camera
Tissue
Application example: adaptive optics
Emission wave
Excitation wave
Image through thick scattering tissue.
Correction element
Image thr. thick tissue + correction element
Undo scattering
Same pattern
Adaptive optics =
overcoming the
fundamental challenge
of optics
No practical algorithm for finding correction element.
Existing approaches: invasive camera from the other side, costly optimization.
Validation Camera
From laser
Notes: And then they invasively placed a camera at the back of the tissue to provide feedback to the algorithm. But in a real biomedical imaging setting, if we could place a camera inside the tissue we could image the fluorescent sources directly, and we wouldn’t need a correction element. Even with this invasive feedback finding the correction element is a very costly process which usually relies on trying thousand intermediate correction elements. And what if the subject is alive? And it is moving?

## Slide 31
Fluorescent Beads
Main system Camera
Tissue
Emission wave
Excitation wave
Correction element
From laser
Results
Validation Camera
Notes: In this research, for the first time, we suggest an algorithm that can recover the correction element non-invasively, and it can do so very very fast.
To do so we need to model the problem analytically. And let me tell you a bit on how we do that.

## Slide 32
Fluorescent Beads
Main system Camera
Tissue
Emission wave
Excitation wave
Correction element
From laser
Results
Validation Camera
Notes: In this research, for the first time, we suggest an algorithm that can recover the correction element non-invasively, and it can do so very very fast.
To do so we need to model the problem analytically. And let me tell you a bit on how we do that.

## Slide 33
Fluorescent Beads
Main system Camera
Tissue
Adaptive optics: analytical model
Emission wave
Excitation wave
Control correction element
Excitation wave
Emission wave
From laser
( )
Transmission operator
Notes: and get a different noise pattern out.

## Slide 34
Fluorescent Beads
Main system Camera
Tissue
Emission wave
Excitation wave
Focus
Control correction element
Excitation wave
Emission wave
Problem: how to obtain feedback on focusing?
Output is yet another speckle pattern.
Adaptive optics: analytical model
From laser
( )
Transmission operator
Notes: Now our goal is to find an illuminating wavefront that focuses into a single point inside the tissue. But note that even if we found such a wavefront, the emission from it still scatters on its way out and we get yet another noisy speckle pattern.
So the main challenge here is how can we know we have focused?
Is there any feedback we can still obtain from its noisy emission?

## Slide 35
Fluorescent Beads
Tissue
Emission wave
Excitation wave
From laser
Results
Validation Camera
Main system Camera
Rapid convergence
initialization
Itr 4
Excitation
Validation camera
Main camera
No mod.
With mod.
Emission
. . .
. . .
. . .
. . .
Notes: we can correct the aberration.
So let’s see what this gives us
As the iteration proceed and the excitation focus into a single bead, the emission is also corrected and we see a sharp spot on the main camera.
So this algorithm converges into a focusing modulation within a very small number of iterations, and this is a big improvement over previous approaches.

## Slide 36
Fluorescent Beads
Tissue
Emission wave
Excitation wave
From laser
Results
Validation Camera
Main system Camera
initialization
Itr 1
Itr 2
Itr 3
Itr 4
Excitation
Validation camera
Notes: Before I talk on how to do that, let me start by showing some results.
In order to better show you what is happening here I put fluorescent beads at the back of the tissue layer and not really inside it, and I put another validation camera behind the tissue, which can image the beads directly. The validation camera does not provide any feedback to the algorithm and is only used to assess its success.
So we start with some random modulation pattern and when this pattern scatters through the tissue we get a wide speckle pattern at the back layer. But based on the image we capture at the main camera we update our modulation and with as little as 4 iterations, the modulated illumination focuses into a single spot behind the tissue.

## Slide 37
Fluorescent Beads
Tissue
Emission wave
Excitation wave
From laser
Results
Validation Camera
Main system Camera
initialization
. . .
Itr 4
Excitation
Validation camera
Filter emission wavelength
Notes: Now to save space I will squeeze this sequence and show only the first and last iterations.
To show you the fluorescent beads themselves I put a bendpass filter so we only see the emission light and not the excitation.

## Slide 38
Fluorescent Beads
Tissue
Emission wave
Excitation wave
From laser
Results
Validation Camera
Main system Camera
initialization
Itr 4
Excitation
Validation camera
Emission
. . .
. . .
Filter emission wavelength
Notes: So you can see that there is a spread of beads here, in the beginning many of them are excited, but as we proceed the excitation light is focused into one spot and as a result only one of the beads emits light.
Now the decision on how to update the modulation is not based on what the validation camera is seeing but on what the main camera from the other side sees, and let’s have a look at what this camera can image

## Slide 39
Fluorescent Beads
Tissue
Emission wave
Excitation wave
From laser
Results
Validation Camera
Main system Camera
initialization
Itr 4
Excitation
Validation camera
Main camera
No mod.
Emission
. . .
. . .
. . .
Notes: We note that even if we manage to focus all the light and excite a single bead, the light will scatter on its way back to the camera, and in the main camera we see yet another speckle pattern.

## Slide 40
Fluorescent Beads
Tissue
Emission wave
Excitation wave
From laser
Results
Validation Camera
Main system Camera
Notes: However if we take the modulation used in the illumination arm and also place the same pattern in the imaging arm we can correct the aberration.

## Slide 41
Main system Camera
Tissue
Output wavefront
Input wavefront
From laser
Coherent iterative phase conjugation
Validation Camera
Reflective particles
output wave
input wave
back-plane wave
Transmission operators
( )
Back-plane wave
input wave
output wave
( )
Back-plane wave
output wave
( )
input wave
Even with focus: output=speckle
 How can we know we have focused?
Phase conjugation principle
back-plane
Notes: With our computer controlled light modulator we can send in various illumination wavefronts. And each such wavefront generates some other wavefront at the back of the tissue.
To model the problem mathematically we consider the transmission matrix of the medium, which describes how each incoming wavefront is mapped into the back plane of the tissue.
Once the wavefront gets to the reflective particles at the back of the tissue it is reflected and scatters back through the tissue and it generates an outgoing wavefront at the main camera.
We consider another transmission matrix To that maps between wavefront at the back plane to wavefonts at the main camera
Overall we will be describing the mapping between incoming illumination to outgoing wavefront at the camera by a transmission matrix T, which is the multiplication of Ti by To.
This model involves some approximation, and we will come back to what we have neglected here in a few slides.
So assuming this Ti To model, we use the principle of optical wave conjugation. It tell us that the wavefront coming out of a point, is the conjugate of the wavefront focusing at it, or namely that To is the transpose of Ti.