## Slide 1
Computational Imaging on the
Electric Grid
Mark Sheinin, Yoav Y. Schechner
Kiriakos N. Kutulakos
to appear in
IEEE CVPR 2017
Viterbi Faculty of Electrical Engineering
Department of
Computer Science

## Slide 2
Natural vs. artificial
illumination
Image: http://maxpixel.freegreatpicture.com
Notes: We spend about half our lives under artificial illumination.

## Slide 3: Artificial illumination is all around us
street lamps
indoors at night
& during daytime
Notes: Artificial light is everywhere, from street lamps at night <click> to our offices and homes at all hours.

## Slide 4: Despite our senses
Notes: To our eyes, these lights appear static. However, in reality<click>

## Slide 5
slow motion by factor 1/130
Despite our senses Artificial illumination is active
Notes: they are constantly flickering…as seen in this
slow motion video of the scene.
The lights in the scene flicker because most of the bulbs are powered by the electric grid.

## Slide 6
Different bulb-types flicker differently
Each bulb type has a unique signature (brightness flicker over time)
sodium
LED2
incandescent
LED1
fluorescent
compact fluorescent (CFL)
slow motion by factor 1/130
Notes: Each bulb type has a unique flicker signature in time.

## Slide 7
AC
Voltage
Example: High-pressure sodium bulb
AC
voltage
Notes: For example, here is the signature of a sodium bulb. These bulbs are common in street lighting.
The spinning clock illustrates the periodic nature of the bulb’s flicker – a bulb’s flicker cycle lasts one-hundredth of a second.

## Slide 8
Different bulb-types flicker differently
Bulbs flicker at twice the voltage frequency
Flicker is at 100Hz or 120Hz , depending on the country
AC voltage
Notes: Bulbs on the grid are powered by alternating current , namely AC. The top graph<click>
shows the AC voltage.
The AC voltage periodically alternates at a frequency of 50 or 60 Hz, depending on the country.<click>
Bulbs flicker at twice this frequency, that is 100 or 120 times each second.
The flicker signature of bulbs depends on the bulb type and electronics.
<click>Here we show raw measurements of flicker signatures for different bulb types.
We call this signature a Bulb Response Function.

## Slide 9
We acquired temporal bulb response functions
for a wide variety of bulbs
DELIGHT: Database of Electrical LIGHTs
Notes: We compiled a database of bulb response functions for many common bulbs.<click>
Our database of electric lights, named DELIGHT, is available online.

## Slide 10
Recognizing AC lights and Grid Phase

## Slide 11
AC electricity is transmitted in three grid phases (0°, 120°, 240°)
Bulb flicker also depends on the outlet’s AC phase
phase
phase
phase
Notes: Power plants supply AC voltage in 3 phases. Each phase is carried by an exclusive power line.
One phase is delayed by a third of the AC period, and is termed “phase 120 degrees”.
Another phase is delayed by two thirds of the AC period, and is termed “phase 240 degrees”.
Bulb flicker thus depends on the AC phase that the bulb is connected to.

## Slide 12
City-scale analysis of the electric grid
A bulb’s type & AC phase can be recognized by analyzing the flicker
Phase
Map of bulbs’ electric phase
| Bulb percentage
Notes: Using the DELIGHT database, the AC phase can be recognized in a scale of a city. <click>
Such city scale grid information is valuable to power grid engineers.

## Slide 13
A bulb’s type & AC phase can be recognized by analyzing the flicker
Bulb recognition
Notes: Let’s see an example.
Here is a closeup on a scene containing many bulbs.

## Slide 14
Unknown source 1
Notes: Let’s look at one bulb.
Below is this bulb’s measured flicker signature.

## Slide 15
Bulb type
Bulb phase
Unknown source 1
Bulb Response Functions
Notes: We discover the bulb type and AC phase by searching for the closest match in the DELIGHT database.

## Slide 16
Bulb type and
grid phase
recovered!
16
High-pressure
Sodium
Sodium, phase 120°
Phase 120°
Bulb Response Functions
Notes: In this case, this is a high-pressure sodium bulb connected to phase 120deg.

## Slide 17
High-pressure
Sodium
Sodium, phase 120°
Sodium, phase 0°
Phase 0°
Bulb Response Functions
Notes: Here is another sodium bulb connected to a different phase,

## Slide 18
Bulb Response Functions
Metal halide
Sodium
Sodium, phase 120°
Sodium, phase 0°
Metal halide, phase 0°
Metal halide, phase 120°
Notes: And here are two bulbs whose type is different than sodium.
Notice that their signature is different from that of sodium bulbs.

## Slide 19
Analyzing scenes having complex lighting

## Slide 20
Imaging on the electric grid
Conventional image
Notes: Lets look at this hallway.
Here is a conventional image.

## Slide 21
Imaging on the electric grid
Sequence: slow motion by factor 1/130
Notes: And here is an image sequence captured using our special camera system
The sequence spans the flicker cycle. This sequence is shown slowed down by factor 130 since it is too fast to be perceived by the naked eye.

## Slide 22
Imaging on the electric grid
Digital amplification of flicker effect
Notes: Here the effect is digitally amplified for better visualization

## Slide 23
Result of digital processing by our algorithm:
How the room would appear if lit only by bulbs connected to electric phase 0°
Imaging on the electric grid
Notes: By processing the sequence captured using our system,
we can reveal hidden information about the scene, and show the scene in a new and different light.
Specifically, the scene can be shown as composed by distinct illumination components.
Here we show a digital rendering of the hallway as if only
bulbs connected to AC phase 0-degrees were active.

## Slide 24
Imaging on the electric grid
Result of digital processing by our algorithm:
How the room would appear if lit only by bulbs connected to electric phase 120°
Notes: And here’s the hallway as if illuminated only by bulbs connected to phase 120-degrees.

## Slide 25
Imaging on the electric grid
Result of digital processing by our algorithm:
How the room would appear if lit only by bulbs connected to electric phase 240°
Notes: And the same for phase 240.

## Slide 26
Digital rendering: switching between phases 0°, 120° and 240°
Imaging on the electric grid
Notes: Let’s switch between the sources again to observe the different illumination components.

## Slide 27
Scene relighting
Result of digital processing by our algorithm:
How the room will appear if sodium bulbs replace CFL bulbs plugged to phase 240°
Notes: Once we have these components, we can digitally recompose the
scene as if some bulbs are exchanged for others, that had not been present when the photos were taken.
For example,<click>
Here we show how the room would appear if bulbs connected to phase 240 are replaced by Sodium bulbs.

## Slide 28
Computational imaging outdoors
conventional photo
4 components
Notes: Here is another example,
This scene has four components

## Slide 29
Component 1: fluorescent
Computational imaging outdoors
Component 2: sodium
Component 3: sodium
Component 4: sodium
Notes: And here we reveal the scene’s illumination components.

## Slide 30
indoor flickering
illumination
outdoor constant
illumination
reflection
indoor scene
outdoor scene
window
camera
outdoor scene
indoor reflection
Notes: Here we observe a scene throw a window. The window causes a reflection.<click> our system separated the outdoor scene <click>from the indoor reflection. The key for doing this is that outdoors, sunlight does not flicker, but indoor lighting is affected by flicker.

## Slide 31
ACam: camera for imaging on the AC grid
Notes: We designed a novel camera, called the ACam, to capture scenes under flickering illumination.

## Slide 32
Conventional camera
long exposure time
camera
camera
lens
Standard exposure
Flicker dynamics not captured
Mark Sheinin, Yoav Y. Schechner, Kyros Kutulakos, CVPR’17
Notes: To capture the scene above during night, a conventional camera shutter must remain open for 1/5 of a second to let enough light reach the sensor.
But, such a long exposure cannot detect the flicker dynamics.

## Slide 33
Conventional camera
short exposure time
single frame
camera
camera
lens
Short exposure
Not enough signal.
Noise dominates
Mark Sheinin, Yoav Y. Schechner, Kyros Kutulakos, CVPR’17
Notes: To capture the flicker dynamics, there is a need for exposure time that is
a fraction of the flicker cycle (marked here in red), if a conventional camera was used.
But, having such a short exposure, the resulting photo would be very noisy, because not enough light would reach the sensor.

## Slide 34
AC imaging principle
Controller
camera
short exposure time
single frame
programmable
mask
camera
lens
Mark Sheinin, Yoav Y. Schechner, Kyros Kutulakos, CVPR’17
Notes: The ACam has a programmable optical shutter (called mask) between the sensor and camera lens.
The camera exposure is set to span hundreds of flicker cycles.
During this long exposure<click> , the programmable mask blocks the light from scene in all times exceptduring specific pre-set brief intervals in each cycle. These pre-set intervals
All correspond to the same fraction of the flicker period.
The ACam is physically connected in an AC outlet. This ensures that
The mask unblocks the light at the precise right instance within each flicker cycle.

## Slide 35
AC imaging principle
Controller
camera
short exposure time
single frame
programmable
mask
camera
lens
Mark Sheinin, Yoav Y. Schechner, Kyros Kutulakos, CVPR’17
Notes: The ACam has a programmable optical shutter (called mask) between the sensor and camera lens.
The camera exposure is set to span hundreds of flicker cycles.
During this long exposure, the programmable mask blocks the light from scene at all times, except
during specific pre-set brief intervals in each cycle.<click> These pre-set intervals
all correspond to the same fraction of the flicker period.
The ACam is physically connected in an AC outlet. This ensures that
The mask unblocks the light at the precise right instance within each flicker cycle.

## Slide 36
Summary
Imaging on the electric grid is uncharted territory
For more information:
http://webee.technion.ac.il/˜yoav/research/ACam.html
http://www.dgp.toronto.edu/ACam
Notes: To summarize, we present a new and exciting way to view scenes, that are illuminated normally by bulbs plugged to the electric grid.
For more information about the project please visit the links below.

## Slide 37
Acknowledgments
The authors thank:
M. O’Toole, Y. Levron, R. Swanson, P. Lehn, Z. Tate, A. Levin, G. Tennenholts
V. Holodovsky, R. Zamir, K. Lavia, I. Talmon and D. Peer.
This research was supported by:
Taub Foundation, Israeli Science Foundation Ollendorff Minerva Center, Mitacs
Canada-Israel Globalink Innovation Initiative, Natural Sciences and Engineering
Research Council of Canada, DARPA - REVEAL.