## Slide 1: The Case for Validating SDN Inputs
Alexander Krentsel12, Rishabh Iyer1, Sylvia Ratnasamy12, Isaac Keslassy3, Rob Shakir2, Anees Shaikh2
1UC Berkeley, 2Google, 3Technion

## Slide 2: No end in sight for WAN outages
Outages continue despite decades of experience and vast literature of best practices:
Simulation/Emulation
  SimBricks [SIGCOMM ’22]
  CrystalNet [SOSP '17]
  Mininet [HotNets ‘10]
Testing:
  NetCastle [NSDI ‘24]
  Ixia (Keysight)
Verification:
  Batfish [NSDI ‘15]
  Header Space Analysis [NSDI ‘12]
  …
Why do they continue?
Time
From Decentralized SDN, SIGCOMM ‘24
1

## Slide 3: Background
2
A
C
B
SDN Controller

## Slide 4: Background
low-level signals
…
external input
A
C
B
Routers
Control Infrastructure
SDN Controller
2
Low-level signals collected from routers and external input
  interface up/down status
  host per-destination sending rates
  …

## Slide 5: Background
A
C
B
Routers
Control Infrastructure
SDN Controller
2
Low-level signals collected from routers and external input
  interface up/down status
  host per-destination sending rates
  …
Aggregated into abstract inputs
  topology:
  demand:
…
low-level signals
abstract inputs
A
C
B
external input

## Slide 6: Background
A
C
B
Routers
Control Infrastructure
SDN Controller
2
Low-level signals collected from routers and external input
  interface up/down status
  host per-destination sending rates
  …
Aggregated into abstract inputs
  topology:
  demand:
SDN controller computes new routes
Routes programmed back into routers
…
low-level signals
abstract inputs
A
C
B
external input

## Slide 7: Key cause: incorrect inputs
Conducted analysis of high-impact SDN WAN outages over past 5 years…
3
A
C
B
Routers
Control Infrastructure
SDN Controller
…
,
⇒ Over 1/3rd root-caused to incorrect inputs.
incorrect: do not reflect reality

## Slide 8: How can inputs be wrong?
Routers
4
A
C
B
Routers
Control Infrastructure
SDN Controller
…
Control system is conceptually simple, but practically complex…
Bugs can happen anywhere that lead to incorrect input produced.

## Slide 9: Real world examples…
5
A
C
B
…
SDN Controller
Demand Collection
Topology Collection
…
Control Infrastructure

## Slide 10: Real world examples…
Outage 1. Bug in demand instrumentation service led to demand collected incorrectly, resulting in partial demand fed to SDN controller. Severe congestion.
A
C
B
…
SDN Controller
Demand Collection
Topology Collection
…
Control Infrastructure
5

## Slide 11: Real world examples…
Outage 1. Bug in demand instrumentation service led to demand collected incorrectly, resulting in partial demand fed to SDN controller. Severe congestion.
Outage 2. Bug causes topology instrumentation service to aggregate topology before all routers report, feeding partial topology to controller.
A
C
B
…
SDN Controller
Demand Collection
Topology Collection
…
Control Infrastructure
5

## Slide 12: Real world examples…
A
C
B
…
SDN Controller
Demand Collection
Topology Collection
…
Control Infrastructure
Auto-drain
Outage 1. Bug in demand instrumentation service led to demand collected incorrectly, resulting in partial demand fed to SDN controller. Severe congestion.
Outage 2. Bug causes topology instrumentation service to aggregate topology before all routers report, feeding partial topology to controller.
Outage 3. Overly-sensitive automatic drain signal gets triggered, incorrectly draining a significant number of perfectly-fine routers. Severe congestion.
5

## Slide 13: Real world examples…
A
C
B
…
SDN Controller
Demand Collection
Topology Collection
…
Control Infrastructure
Outage 1. Bug in demand instrumentation service led to demand collected incorrectly, resulting in partial demand fed to SDN controller. Severe congestion.
Outage 2. Bug causes topology instrumentation service to aggregate topology before all routers report, feeding partial topology to controller.
Outage 3. Overly-sensitive automatic drain signal gets triggered, incorrectly draining a significant number of perfectly-fine routers. Severe congestion.
(small) Outage 4. New router OS rollout for vendor X causes telemetry messages to oscillate between 0 and actual. Triggers flap protection drains.
5

## Slide 14: Why is it not caught today?
Eng. teams check for outliers/anomalies
6
A
C
B
Control Infrastructure
SDN Controller
…
Eng. teams check for outliers/anomalies, but this misses the underlying issue:
…incorrect inputs are often possible values but not current values.

## Slide 15: Why is it not caught today?
, …
Eng. teams check for outliers/anomalies, but this misses the underlying issue:
…incorrect inputs are often possible values but not current values.
6
A
C
B
Control Infrastructure
SDN Controller
…
No way to distinguish from input alone.
Requires an alternative approach…

## Slide 16: Validating controller inputs
SDN Controller
Goal: validate that the abstract inputs agree with reality.
C
Control Infrastructure
…
A
B
,
Reality
7
What is reality?
Whatever we know is happening at the routers, “ground truth”

## Slide 17: Rich view of reality
SDN Controller
Many low-level signals available:
Interface byte counters
Packet drop counters
Forwarding entries
Bidirectional Forwarding Detection (BFD) link monitoring updates
Probes
…
C
Control Infrastructure
…
A
B
,
Reality
8
Recursive problem: all sources complex, how can we trust the signals?

## Slide 18: Making low-level signals trustworthy
SDN Controller
C
Control Infrastructure
…
A
B
9
Network signals are naturally interconnected.
→ Actions reflected in multiple measurements.

## Slide 19: Making low-level signals trustworthy
SDN Controller
C
Control Infrastructure
…
A
B
9
Network signals are naturally interconnected.
→ Actions reflected in multiple measurements.
16
16
87
87

## Slide 20: Making low-level signals trustworthy
SDN Controller
C
Control Infrastructure
…
A
B
9
17
Network signals are naturally interconnected.
→ Actions reflected in multiple measurements.
16
87
87

## Slide 21: Making low-level signals trustworthy
SDN Controller
C
Control Infrastructure
…
A
B
9
17
Network signals are naturally interconnected.
→ Actions reflected in multiple measurements.
17
87
87

## Slide 22: Making low-level signals trustworthy
SDN Controller
C
Control Infrastructure
…
A
B
9
17
Network signals are naturally interconnected.
→ Actions reflected in multiple measurements.
17
88
87

## Slide 23: Making low-level signals trustworthy
SDN Controller
C
Control Infrastructure
…
A
B
9
17
Network signals are naturally interconnected.
→ Actions reflected in multiple measurements.
17
88
88

## Slide 24: Making low-level signals trustworthy
SDN Controller
C
Control Infrastructure
…
A
B
9
17
Network signals are naturally interconnected.
→ Actions reflected in multiple measurements.
17
88
88

## Slide 25: Making low-level signals trustworthy
SDN Controller
9
Practically: can collect all known signals, and catch & repair inconsistencies: “harden”
…
B
C
A
Control Infrastructure
Harden
Network signals are naturally interconnected.
→ Actions reflected in multiple measurements.
Use redundancy to check that reported network state agrees with itself, then even self-repair.

## Slide 26: Input validation: agreement with high-level inputs
Once we have hardened signals, can use them to do input validation.
Check that expected relations hold between abstract inputs and low-level signals.
10
SDN Controller
…
B
C
A
Control Infrastructure
Harden

## Slide 27: Input validation: agreement with high-level inputs
Once we have hardened signals, can use them to do input validation.
Check that expected relations hold between abstract inputs and low-level signals.
10
SDN Controller
…
B
C
A
Control Infrastructure
Harden
Validation
We present our system, Hodor, that performs continuous validation.

## Slide 28: Hodor: (1) Hardening low-level signals
Many examples of redundancy in network data…
11

## Slide 29: Hodor: (1) Hardening low-level signals
Many examples of redundancy in network data…
R1. Symmetry across two ends of link: bytes in = bytes out.
A
B
→ Bytes Sent
Bytes Received →
11

## Slide 30: Hodor: (1) Hardening low-level signals
Many examples of redundancy in network data…
R1. Symmetry across two ends of link: bytes in = bytes out.
R2. Flow conservation across ports: sum in = sum out at a router.
A
→ Bytes Sent
← Bytes Received
Bytes Sent ←
Bytes Received →
Bytes Sent ←
Bytes Received →
11

## Slide 31: Hodor: (1) Hardening low-level signals
Many examples of redundancy in network data…
R1. Symmetry across two ends of link: bytes in = bytes out.
R2. Flow conservation across ports: sum in = sum out at a router.
R3. Alternative signal substitutes: link down ⇒ intf count = 0.
A
B
Interface up:
Bytes Received: 0
11

## Slide 32: Hodor: (1) Hardening low-level signals
Many examples of redundancy in network data…
R1. Symmetry across two ends of link: bytes in = bytes out.
R2. Flow conservation across ports: sum in = sum out at a router.
R3. Alternative signal substitutes: link down ⇒ intf count = 0.
R4. Manufactured signals: probe confirms link up/down.
A
B
Interface up:
Probe Success
11

## Slide 33: Hodor: (1) Hardening low-level signals
Many examples of redundancy in network data…
R1. Symmetry across two ends of link: bytes in = bytes out.
R2. Flow conservation across ports: sum in = sum out at a router.
R3. Alternative signal substitutes: link down ⇒ intf count = 0.
R4. Manufactured signals: probe confirms link up/down.
…
A
B
→ 75
2 →
75 →
75 →
12

## Slide 34: Hodor: (1) Hardening low-level signals
Many examples of redundancy in network data…
R1. Symmetry across two ends of link: bytes in = bytes out.
R2. Flow conservation across ports: sum in = sum out at a router.
R3. Alternative signal substitutes: link down ⇒ intf count = 0.
R4. Manufactured signals: probe confirms link up/down.
…
A
B
→ 75
2 →
75 →
75 →
12

## Slide 35: Hodor: (1) Hardening low-level signals
Many examples of redundancy in network data…
R1. Symmetry across two ends of link: bytes in = bytes out.
R2. Flow conservation across ports: sum in = sum out at a router.
R3. Alternative signal substitutes: link down ⇒ intf count = 0.
R4. Manufactured signals: probe confirms link up/down.
…
A
B
→ 75
2 →
75 →
75 →
12

## Slide 36: Hodor: (1) Hardening low-level signals
Many examples of redundancy in network data…
R1. Symmetry across two ends of link: bytes in = bytes out.
R2. Flow conservation across ports: sum in = sum out at a router.
R3. Alternative signal substitutes: link down ⇒ intf count = 0.
R4. Manufactured signals: probe confirms link up/down.
…
A
B
75 →
75 →
75 →
12

## Slide 37: Hodor: (2) Agreement with high-level inputs
System expert can define relationships between low-level observations and high-level abstract inputs.
Ex: for validating demand, sum of demand to a node == egress interface count
Hodor verifies that such relations hold for the given inputs and trusted snapshots.
D =
A
B
75 →
C
75 →
B
A
B
C
A
C
13

## Slide 38: Active questions
How do we build this?
  Inconsistent data due to snapshot time skew
Alternative unsupervised learning approaches? Other strategies?
  Masked autoencoders, symbolic regression
Right space of response actions?
How prevalent are incorrect inputs in other control systems?
  Anecdotally, heard of similar problems for cloud tenant networks, datacenter networks
Alexander Krentsel – akrentsel@berkeley.edu
Paper Link